## Slide 1
Claire Dross, Pavlos Efstathopoulos, David Lesens, David Mentré and Yannick Moy
Embedded Real Time Software and Systems – February 5th, 2013
Rail, Space, Security: Three Case Studies for SPARK 2014

## Slide 2
SPARK 2014

## Slide 3: Ada 2012 and SPARK 2014
programming language for long-lived embedded critical software
Ada subset for formal verification
programming by contract
practical formal verification

## Slide 4: SPARK 2014 Value Proposition
Functional Requirement
Functional Verification
Software Architecture
Software Architecture Verification
Unit Requirements
Unit Verification
Code
Robustness Verification

## Slide 5: SPARK 2014 Value Proposition (DO-178C Version)
System Requirements
High Level Requirements
Low Level Requirements
Software Architecture
Source Code
Executable Object Code
Compliance Robustness
Property Preservation
Software architecture
is consistent
Accuracy
Consistency

## Slide 6: SPARK 2014 Contracts
Contract = agreement between client & supplier
Program
caller & callee
Contract = agreement between client & supplier
Dynamic Verification
Formal Verification

## Slide 7
Case Studies

## Slide 8
Case study 1: Train Control Systems
David Mentré

## Slide 9: openETCS
Open Source  no vendor lock-in
Model based (SysML)
Formal methods  Strong guaranties of correctness
“Open Proofs”  Everybody can re-check

## Slide 10: Formalization of the Correctness of Step Functions
Has_Same_Delimiters?
Get_Value?
Minimum_Until_Point?
Restrictive_Merge?

## Slide 11: Results
SPARK 2014 very good for:
Expressing objects of the requirements
Readability of the specifications
Automatic proof of absence of run-time errors
Automatic proof of simple functional contracts
Dynamic verification of contracts and assertions
SPARK 2014 is not good for:
Proving existing code without any modifications
Proving automatically complex functional contracts
Areas requiring improvements:
Possibility to prove some properties interactively (in 2014 roadmap)
Better diagnostic for incomplete loop invariants (in 2014 roadmap)
Training for developers to use proof tools (available in SPARK Pro subscription)
Workflow to make efficient use of developers’ time (in progress)

## Slide 12
Case study 2: Flight Control and Vehicle Management in Space
David Lesens

## Slide 13: On Board Control Procedure
On-board control procedure
  Software program designed to be executed by an OBCP engine, which can easily be loaded, executed, and also replaced, on-board the spacecraft
OBCP code
  Complete representation of an OBCP, in a form that can be loaded on-board for subsequent execution
OBCP engine
  Application of the on-board software handling the execution of OBCPs
OBCP language
  Programming language in which OBCP source code is expressed by human programmers

## Slide 14: Formalization of the Correctness of 1505 Functions
Event1
Event2
Event3
Not detected
Not detected
Detected
procedure Reset_Event_Status (Event : in T_Event) with
Post =>
not Event_Status (Event).Detection and
(for all Other_Event in T_Event =>
(if Other_Event /= Event then
Event_Status (Other_Event) = Event_Status'Old (Other_Event)));
Example:
A list of event detection statuses
Request to reset the detection status for Event
The detection status is unchanged
Post-condition
The detection of event is reset
For all other events

## Slide 15: Automatic Proof Results
Numerical control/command algorithms
Mission and vehicle management
Formal Verification of Aerospace Software, DASIA 2013, http://www.open-do.org/wp-content/uploads/2013/05/DASIA_2013.pdf
Part | # subprograms | # checks | % proved
Math library | 15 | 27 | 92
Numerical algorithms | 30 | 265 | 98
Part | # subprograms | # checks | % proved
Single variable | 85 | 268 | 100
List of variables | 140 | 252 | 100
Events | 24 | 213 | 100
Expressions | 331 | 1670 | 100
Automated proc | 192 | 284 | 74
On board control proc | 547 | 2454 | 95

## Slide 16: Results
SPARK 2014 very good for:
Proof of absence of run-time errors
Correct access to all global variables
Absence of out-of-range values
Internal consistency of software unit
Correct numerical protection
Correctness of a generic code in a specific context
SPARK 2014 is good for:
Proof of functional properties
Areas requiring improvements:
Sound treatment of floating-points (done)
Support of tagged types (in 2014 roadmap)
Helping user with unproved checks (in 2014 roadmap)

## Slide 17
Case study 3: Biometric Access to a Secure Enclave
Pavlos Efstathopoulos

## Slide 18: Tokeneer

## Slide 19: Formalization of the “Admin” Package
Dataflow
Information flow
Refinement
Functional contracts
User guidance
Assumptions

## Slide 20: Results
SPARK 2014 very good for:
Expressing specification-only code
Analysis of code that was not analyzable with SPARK 2005
Automating proofs with fewer user efforts
Expressing complete functional behavior of functions
Readability of the formal specifications
Uncovering corner cases related to run-time checks
Areas requiring improvements:
Summary of proof results (done)

## Slide 21
Lessons Learned

## Slide 22: SPARK 2014 Strengths
executable
contracts
better
automation
of proofs
expressive
specification
language

## Slide 23: SPARK 2014 Challenges
static debugging
of contracts
need
expert advice
sometimes
code and specifications must be adapted

## Slide 24
SPARK in 2014

## Slide 25: Roadmap
Now available as beta
First release April 2014
  See http://www.adacore.com/sparkpro
  and http://www.spark-2014.org