## Slide 1
SPARK:
Retours d'expérience
et intérêt en transport
Présenté par Yannick Moy

## Slide 2: SPARK – Flow Analysis
Specification of effects
Flow analysis
Program implements specification

## Slide 3: SPARK – Proof
Specification of properties
Proof
Program implements specification

## Slide 4: Formal Program Verification
C
Ada
1999
Caveat
2008
2014
1987
SPARK
2013
Formal Verification of Avionics Software Products, Souyris et al., Airbus, FM 2009
Are We There Yet? 20 Years of Industrial Theorem Proving with SPARK, Chapman and Schanda, Altran, ITP 2014
1997
C130J
2002
Airbus

## Slide 5: Key Features - Integration
Build-Test-Prove
all in the same IDEs

## Slide 6: Key Features - Integration
Contracts are code

## Slide 7: Key Features - Automation

## Slide 8: Key Features - Automation

## Slide 9: Key Features - Interaction
Counterexample
Path

## Slide 10: Levels of Software Assurance

## Slide 11: Stone Level
Strong semantic coding standard
Program respects all the SPARK language legality rules
Enforces safer use of language features:
  Restricted concurrency (Ravenscar profile)
  Expressions and functions without side-effects
Forbids language features that make analysis difficult:
  Unrestricted pointers
  Exception handlers

## Slide 12: Bronze Level
Initialization and correct data flow
Program passes SPARK flow analysis without violations
Detects programming errors:
  Read of uninitialized data
  Problematic aliasing between parameters
  Data race between concurrent tasks
Checks user specifications:
  Data read or written
  Flow of information from inputs to outputs

## Slide 13: Silver Level
Absence of run-time errors
Program passes SPARK proof without violations
Detects programming errors:
  Divide by zero
  Array index out of bounds
  Integer, fixed-point and floating-point overflow
  Integer, fixed-point and floating-point range violation
  Explicit exception raised
  Violation of Ceiling Priority Protocol

## Slide 14: Gold Level
Proof of key integrity properties
Program passes SPARK proof without violations
Checks user specifications:
  Type invariants (weak and strong)
  Preconditions
  Postconditions
Checks correct use of OO wrt Liskov Substitution Principle

## Slide 15: Platinum Level
Proof of full functional correctness
Program passes SPARK proof without violations
Checks complete user specifications:
  Type invariants (weak and strong)
  Preconditions
  Postconditions
Checks loop termination (loop variant)

## Slide 16: Software Assurance Levels

## Slide 17: Industrial Practice

## Slide 18: Established Practice at Altran UK
Software Integrity Level |  | SPARK Software Assurance Level |  |  | 
DAL | SIL | Bronze | Silver | Gold | Platinum
A | 4 |  |  |  | 
B | 3 |  |  |  | 
C | 2 |  |  |  | 
D | 1 |  |  |  | 
E | 0 |  |  |  | 

## Slide 19: Past Projects at Altran UK
C130J: 1996 - now
Bronze (Lockheed Martin) and Gold (UK RAF and BAE Systems)
iFACTS: 2006 - now
Silver (NATS)
SHOLIS: 1995
DEFSTAN 00-55 SIL4
First Gold

## Slide 20: Adoption Experiments at Thales
Use case 1: porting to new platform context: 300 klocs radar software target: Stone level significant manual refactoring (several days) on the way to completion on 300 klocs | Use case 2: demonstrate compliance to LLR context: small numerical function target: Gold level difficulties in expressing suitable context property was not proved automatically
Use case 3: identify and fix weakness context: 100s slocs code generator target: Gold level half a day to reach Silver property related to inner memory bounds two days to reach Gold | Use case 4: guarantee safety properties context: 7 klocs command & control target: Gold level one day to reach Silver property expressed as automaton four days to reach Gold

## Slide 21: Adoption Guidelines with Thales
For every level, we present:
  Benefits, Impact on process, Costs and limitations
  Setup and tool usage
  Violation messages issued by the tool
  Remediation solutions
Guidance was put to test:
  During adoption experiments at Thales
  On example (SPARK tool) presented in last section

## Slide 22: Features that Matter

## Slide 23: Stone Level – Large Language Subset
SPARK_Mode => On
  Ada types, expressions, statements, subprograms
    SPARK_Mode => Off
      Ada pointers
      Ada exception handlers
  Ada generics
  Ada object orientation
  Ada concurrency
SPARK_Mode => On
  Ada types, expressions, statements, subprograms
    SPARK_Mode => Off
      Ada pointers
      Ada exception handlers
  Ada generics
  Ada object orientation
  Ada concurrency

## Slide 24: Stone Level – Large Language Subset
SPARK_Mode => On
  Ada types, expressions, statements, subprograms
    SPARK_Mode => Off
      Ada pointers
      Ada exception handlers
  Ada generics
  Ada object orientation
  Ada concurrency
  Ada pointers
work in progress to include safe Rust-like pointers in SPARK
SPARK_Mode => On
  Ada types, expressions, statements, subprograms
    SPARK_Mode => Off
      Ada pointers
      Ada exception handlers
  Ada generics
  Ada object orientation
  Ada concurrency

## Slide 25: Bronze/Silver Level – Generation of Contracts
Example: SPARKSkein Skein cryptographic hash algorithm (Chapman, 2011)
target: Silver level
initial version (SPARK 2005) | current version (SPARK 2014)
41 non-trivial contracts for effects and dependencies | 1 – effects and dependencies are generated
31 conditions in preconditions and postconditions on internal subprograms | 0 – internal subprograms are inlined
43 conditions in loop invariants | 1 – loop frame conditions are generated
23 annotations to prevent combinatorial explosion | 0 – no combinatorial explosion

## Slide 26: Silver/Gold Level – Combination of Provers

## Slide 27: Silver/Gold Level – Combination of Provers
Example: Safe bounds on trajectory computation (submitted to VSTTE 2017)
target: Gold level

## Slide 28: Gold/Platinum Level – Auto-Active Verification
2
1
4
5
3
Example: Functional correctness of red-black trees (NFM 2017)
target: Platinum level
Auto-Active = portmanteau of Automatic and interActive
supported by ghost code: contracts, loop invariants,
intermediate assertions, lemma procedures
ghost code used to:
  define model of data used in specifications
  prove intermediate lemmas (e.g. for inductive proofs)
  provide witness for property (e.g. for transitivity relation)

## Slide 29: Gold/Platinum Level – Auto-Active Verification
Chart: 
| Binary Trees | Search Trees | Red-black Trees
Code | 92 | 127 | 67
Contract | 250 | 188 | 118
Ghost | 548 | 780 | 325

## Slide 30: Use in Certification

## Slide 31: Avionics – DO-178C and DO-333
AdaCore Technologies
for DO‑178C / ED‑12C
https://www.adacore.com/books/do-178c-tech

## Slide 32: Railway – EN 50128
AdaCore Technologies
for CENELEC EN 50128:2011
https://www.adacore.com/books/cenelec-en-50128-2011
D.34 Interface Testing
D.35 Language Subset
D.38 Modular Approach
D.49 Strong Typing
D.53 Structured Programming
D.54 Suitable Programing Languages
D.2 Analyzable Programs
D.4 Boundary Value Analysis
D.10 Data Flow Analysis
D.14 Defensive Programming
D.18 Input Partition Testing
D.24 Failure Assertion Programming
D.28 Formal Methods

## Slide 33: Automotive – ISO 26262
working on a booklet
AdaCore Technologies
for ISO 26262
Table 1 — Topics to be covered by modelling and coding guidelines
Table 2 — Notations for software architectural design
Table 6 — Methods for the verification of the software architectural design
Table 9 — Methods for the verification of software unit design and implementation
Table 11 — Methods for deriving test cases for software unit testing
Table 13 — Methods for software integration testing
Table 14 — Methods for deriving test cases for software integration testing

## Slide 34: Conclusion

## Slide 35: Levels of Software Assurance
From strong semantic coding standard to full functional correctness
Every level implicitly builds on the lower levels
Lower levels require lower costs/efforts
Good match from DAL/SIL to Bronze-Silver-Gold-Platinum
Good match to certification objectives in transport
Adoption greatly facilitated by detailed level-specific guidance

## Slide 36: SPARK Resources
SPARK toolset
http://www.adacore.com/sparkpro http:// www.adacore.com/community
SPARK adoption guidance
www.adacore.com/knowledge/technical-papers/implementation-guidance-spark
SPARK blog and resources (User’s Guide)
http://www.spark-2014.org
SPARK online training
http://u.adacore.com