## Slide 1
Quentin Ochem
Technical Account Manager
SPARK 2014 Towards a Formal Proof Environment for DO-178C

## Slide 2
A few words on DO-178C
… yes again …

## Slide 3: DO-333 – Formal Methods Supplement for DO-178C
DO-178B was centered on testing – replacement by formal proof required extra justification with the authorities
DO-178C is still centered on testing but… DO-333 supplement allows to replace some verifications (reviews, tests, analysis) by formal methods
Activities and objectives are replaced
4 new objectives on Table 3, 4, 5 (HLR, LLR, Code)
  Formal cases and procedures are correct
  Formal analysis results are correct and discrepancies are explained
  Requirement formalization is correct
  Formal method is correctly defined, justified and appropriate
7 new objectives on Table 7 (Verification of the Verification)

## Slide 4: Disclaimer, FM 6.7
Tests executed in target hardware are always required to ensure that the software in the target computer will satisfy the high-level requirements.

## Slide 5
System Requirements
High Level Requirements
Low Level Requirements
Software Architecture
Source Code
Executable Object Code
DO-178C Verification Activities

## Slide 6
System Requirements
High Level Requirements
Low Level Requirements
Software Architecture
Source Code
Executable Object Code
What we are interested here
Compliance Robustness
by Testing

## Slide 7
System Requirements
High Level Requirements
Low Level Requirements
Software Architecture
Source Code
Executable Object Code
What we are interested here
Compliance Robustness
Property Preservation
by Formal Proof

## Slide 8: Replacing Low Level Testing by Formal Proof
Ensures that specifications / requirements / properties are expressed in a non-ambiguous way
Increases confidence in functional aspects of the code
  All cases are formally proven
Applicable both to normal range test cases and robustness cases

## Slide 9
A few words on SPARK
… yes again …

## Slide 10: What is SPARK 2014?
SPARK is a Ada-based language and toolset allowing to perform formal analysis
  Absence of run-time errors
  Data Flow and Information Flow analysis
  Correctness with regards to contracts
SPARK is based on a provable Ada 95 subset and additional annotations
The Ada 2012 language extends the Ada 95 / 2005 definition, including requirements from SPARK language
SPARK 2014 is a new language and toolset based on Ada 2012 including
  A much wider support for the Ada constructions
  A format for contract associated with formal and executable semantics
  An environment ready for local type substitutability proof
  An environment ready for low-level requirement compliance and robustness verification
  An integration environment between unit testing and unit proof

## Slide 11: Ada 2012 Additions for Contract Specification
Contracts on subprograms
Contracts on types
New expressions such as quantifiers
All of these construction are provided with dynamic semantics by Ada 2012
All of these construction are provided with proof semantics by SPARK 2014
G : Integer; procedure P (X, Y : Integer) with Pre => X + Y > 0; Post => G = G’Old + 1;
type Even is new Integer with Dynamic_Predicate => Even mod 2 = 0;
type Sorted_Array is array (Integer range <>) of Integer with Dynamic_Predicate => Sorted_Array’Size <= 1 or else (for all I in Sorted_Array’First .. Sorted_Array’Last – 1 => Sorted_Array (I) <= Sorted_Array (I + 1));

## Slide 12
A few words on DO-178C and SPARK 2014
…

## Slide 13
System Requirements
High Level Requirements
Low Level Requirements
Software Architecture
Source Code
Executable Object Code
Back to DO-333
Compliance Robustness
Property Preservation
by Formal Proof
SPARK 2014
?

## Slide 14: About Property Preservation
If formal analysis is done on the Source Code, then some complementary analysis needs to be done to show property preservation between the source code and executable object code
This can be done through analysis on a sample representative of the coding standard, close to Source to Object traceability study
In SPARK 2014, properties are expressed in the form of executable contract, could we take advantage of that?
Note: required from level A to D
“Complementary analysis shows property preservation between the Source Code and the EOC. […] This is similar to the way that coverage metrics gained from Source Code can be used to establish the adequacy of tests to verify the target system. […]’

## Slide 15: FM 6.7.1.1 Requirement-based coverage analysis
This is similar for test cases, e.g. verifying that the formal analysis cases are complete
a. Analysis, using the associated Trace Data, to confirm that formal analysis cases exist for each software requirement.
b. Analysis to confirm that formal analysis cases satisfy the criteria of normal range and robustness criteria as defined in sections FM.6.7, items a and b.
c. Resolution of any deficiencies identified in the analysis. Possible solutions are adding or enhancing formal analysis cases.

## Slide 16: What About Structural Coverage?
Testing is verifying samples of the execution behavior. The structural coverage criteria is an accepted means to answering the question “has there been enough test”
Formal proof is verifying the correctness of the application for all possible inputs, so this criteria doesn’t make sense anymore
We need an criteria to answer the question “is the formal proof accurate?”
  Shortcomings in verifications cases
  Inadequacies in software requirements
The question of dead / extraneous / unused code remains as well

## Slide 17: FM 6.7.1.2 Complete Coverage of Each Requirement
A formal proof is always based on a number of assumptions
  To complete the mathematical proof
  To describe the boundaries of the module
  Etc.
The reliability of the proof is directly related to the fact that these assumptions are
  Correctly listed
  Correctly analyzed
  Correctly verified (by reviews, testing…)

## Slide 18: FM 6.7.1.3 Completeness of the Set of Requirements
Requirements should be complete with regards to the expected function
For all input, the required output has been covered
For all output, the required input has been covered
SPARK 2014 toolset can proof that all values for all input have been taken into account by output conditions
SPARK 2014 allows to simplify the description of input / output relations through the Contract_Case aspect
Verifying that all possible output can be done through manual review

## Slide 19: FM 6.7.1.3 Completeness of the Set of Requirements
Contract Cases allows to partition the post-condition space making it easier to describe the output
This eases description of post condition, and eases review and analysis on the output
Complete partition of the input space is verified
type Op_Type is (Add, Sub, Mul, Div); function Op (Kind : Op_Type; X, Y : Integer) return Integer is when Contract_Case => (Requires => Kind = Add Ensures => Op’Result => X + Y), Contract_Case => (Requires => Kind = Sub Ensures => Op’Result => X - Y), Contract_Case => (Requires => Kind = Mul Ensures => Op’Result => X * Y), Contract_Case => (Requires => Kind = Div Ensures => Op’Result => X / Y),

## Slide 20: Side Note – Test Cases
SPARK 2014 can integrate test with proof, Test_Case is the element corresponding to Contract_Cases
Opens additional doors to integration with formal proof and tests, to be continued…
type Op_Type is (Add, Sub, Mul, Div); function Op (Kind : Op_Type; X, Y : Integer) return Integer is when Test_Case => (Requires => Kind = Add Ensures => Op’Result => X + Y), Test_Case => (Requires => Kind = Sub Ensures => Op’Result => X - Y), Test_Case => (Requires => Kind = Mul Ensures => Op’Result => X * Y), Test_Case => (Requires => Kind = Div Ensures => Op’Result => X / Y),

## Slide 21: FM 6.7.1.4 Detection of Unintended Dataflow Relationships
The information flow in the source code should comply with the one described in the requirements, that is
  All data usage (parameters, global) is specified and verified
  All data dependency is specified and verified
SPARK 2014 provides data flow analysis that verifies that all input and output data has been specified, including side effect
SPARK 2014 provides information flow analysis that verifies that the dependencies between all input and output is defined
SPARK 2014 proves that the data flow and information specified is indeed implemented

## Slide 22: FM 6.7.1.4 Detection of Unintended Dataflow Relationships
Res : Integer; procedure P (X, Y : Integer) with Global => (Out => G), Depends => ((G) => (X, Y));
G is a global variable written
No other global variable is accessed or modified
The value of G is computed from the value of X and Y

## Slide 23: FM 6.7.1.5 Detection of Extraneous Code
Unreachable or dead code is not expected to be found by formal proof, so needs to be by review or other means of analysis, but…
… given that all input have an output and all output have an input
… given that all data and data relations have been described and verified
… statements that are not “covered” are statements that cannot contribute to the output of the program and that can’t be reached by the input
So manual review or non-formal proof analysis is appropriate

## Slide 24
One word on DO-332
… I know …

## Slide 25: Local Type Substitutability (part of DO-332, OOT supplement)
Local Type Substitutability is a new objective in DO-332, allowing the use of object orientation and dispatching calls
It relies on a demonstration of consistency between overriding methods which can be verified by testing or formal analysis
Given a dispatching call from a Root type to one of its methods …
… at run-time, it’s OK to call an overridden method of a child if
  The child method precondition does not require additional properties
  The child method postcondition provides at least as many properties
Root.Method

## Slide 26: Local Type Substitutability with SPARK and Formal Proof
On top of correctness of pre and post conditions, we need to demonstrate that
  Parent preconditions imply Child preconditions
  Child postconditions imply Parent postconditions
type Abstract_Plane is tagged record Speed : Integer; Landed : Boolean; end record; procedure Land (V : Root) with Pre => V.Speed <= 10.0, Post => V.Landed; type My_Plane is new Abstract_Plane with record Gears_Deployed : Boolean; end record; overriding procedure Land (V : Child) with Pre => V.Speed <= 15.0, Post => V.Landed and V.Gears_Deplyed;
V <= 10.0  V <= 15.0
{V.Landed, V.Gears_Deployed}  V.Landed

## Slide 27
A few words from the Marketing Department
… yes again …

## Slide 28: Conclusion
SPARK 2014 is a COTS product and methodology allowing progressive introduction of formal methods to a DO-178C certified project
  Soon available as beta
  First release Q1 2014
  See http://www.adacore.com/spark2014
SPARK 2014 is a major evolution of a technology that has over 20 years of track record
  See http://www.adacore.com/sparkpro for information on the previous version of the technology
SPARK 2014 is following a methodology that has successfully applied by the industry precursors
  See IEE Software paper about Airbus and Dassault experience (http://www.open-do.org/wp-content/uploads/2013/04/IEEE_Software_Formal_Or_Testing.pdf)

## Slide 29
… thank you …